P_max=(544/6)(fluid_usage_per_tick)(60 ticks)(effectivity)
* P_max is the power generated in KW from converting whatever fluid at maximum performance.
* fluid_usage_per_tick and effectivity are taken from lua files as defined by the mod author for their particular engines.
* 544/6 is the maximum energy conversion rate of the game, ~90.6 KJ/s.
                                         P_max
Actual-Fluid-usage-per-second= ------------------------
               [(heat_capacity)(Fluid-temperature - default_temperature)]
* This is the actual fluid usage rate by the generator in the game when working.
* heat_capacity and default-temperature are taken from lua files as defined by the mod author for that particular fluid.
* Fluid-temperature is the current fluid temperature value, it could be lower than the maximum value defined for that fluid.